## Slide 1: Generating a Data-Driven Surrogate Model for Machine Damage Accumulation
Problem 1
UB Manufacturing & Artificial Intelligence Team (UBMAIT)
Dustin Bielecki & Darshil Patel, Raj Khawale
University at Buffalo, NY (UB)

## Slide 2: Agenda
  Problem Description
  Approach
  Results & Discussion
  Summary

## Slide 3: PROBLEM DESCRIPTION

## Slide 4: Introduction
Objective : To create a data driven model that rapidly outputs damage accumulation values based on other parameter measurements for manufacturing facilities of Bernard M. Gordon Learning Factory
Implicit Challenges
Can we construct data driven digital twin for forecasting?
Can we identify signals in data which have most impact?
Can we reduce machine damage by focusing on specific parameters?
1) “Deep learning-based feature engineering for stock price movement prediction” Wen Long, Zhichen Lu, Lingxiao Cui.
2) “Integrating the Digital Twin of the manufacturing system into a decision support system for improving the order management process”, Kunath, M., & Winkler, H.

## Slide 5: Datasets
Two weeks of data for 5 machines (3 Bridgeport mills, 1 lathe, 1 drill press) is provided for training our model
Training Inputs
(11 variables)
Peak acceleration
RMS velocity
Ambient Temperature
Peak velocity
Battery Voltage
……..
Output
(2 variables)
Damage accumulation
- X-axis
- Y-axis
Data-Driven Model

## Slide 6: APPROACH

## Slide 7: Approach – Initial
Initially used DNN with residual layers
values were low (~0.8 on train, ~0.7 on test)
Observed damage accumulation values
  Peak vs other corresponding to on/off
Created a classification based approach

## Slide 8: Approach - Classification
Inputs are fed into an SVM for on/off classification
Machine status off defaults the damage accumulation values to maximum likelihood of the data
Machine status on feeds the
SVM
ResNN
MLE
Inputs
Machine on
Machine off

## Slide 9: Approach - NN
Network uses the full 11 inputs
Hidden layer of 40 nodes
3 Residual blocks
Final hidden layer of 10 nodes
2 node output representing the damage accumulation

## Slide 10: RESULTS & DISCUSSION

## Slide 11: Results
Training performance
  Samples were run for 10,000 epochs
  The mean squared error was still seemingly high due to limited number of samples
    This is still much better than assuming average values
  Dataset was actually sparse
Epoch
Mean Squared Error
Mean Squared Error vs Epoch

## Slide 12: Results – r2
  Bridgeport 1
    0.879 on reduced data, 0.932 on full dataset
  Bridgeport 2
    -1.493 on reduced data, 0.959 on full dataset
  Bridgeport 3
    -35.75 on reduced data, 0.942 on full dataset
  Drill
    -7.194 on reduced data, 0.906 on full dataset
  Lathe
    -2.647 on reduced data, 0.927 on full dataset

## Slide 13: Findings and Discussion
How your approach/model/simulation helps address the challenges and solve the problem?

## Slide 14: SUMMARY

## Slide 15: Closure & Insights